ID 1043345 : S01 camera operation manual

The device consists of a board with a slot for a memory card TF.

ON-OFF switch

USB port

3 push-buttons ( under the protective film)

A ribbon cable with the camera.

A microphone

Normally operate the camera by remote control, but it can also be operated with the hidden buttons on the unit.

1 Start up:

Put the power switch in the ON position. (move the lever towards the red cable).

The RED an BLUE Leds are located inside the unit and can be seen by looking into the unit near the microphone.

To place the unit in standby mode, you must press  long the A button of the remote control.

After pressing:

The red LED goes on and stays on

The blue LED goes on for three (3) seconds.

The device vibrates long

A other push on the A button of the remote control put the device in a sleep mode

Blue LED flashes 3 times

Red LED goes OFF

The device vibrates short

2 Camera :     constantly recording video

The device has to be in stand by mode, so the red LED is on.

Press button B of the remote control to start camera recording

Red led flashes 3 times and goes out

The device vibrates short and make video recordings.

Stop recording with the camera by pressing the B button again

Red Led comes on and stays on.( stand by mode)

The device vibrates two times.

3 Picture:

A picture can be taken by pressing the button C on remote control when the device is in stand by mode .

Blue LED flashes once

Red goes out and on again

The device vibrates short

Picture is taken every time the button C of the remote control is operated

4 Motion detection:

This option can be used for stand alone working. The camera will make a video of 1 min every time a movement is detected.

When the device is in standby mode, then a short press the D button on the remote control brings the unit in the motion detection mode.

The blue LED blinks twice and turns off.

The red LED turns off.

The device vibrates two times ( motion detection ON)

Press again the button D to bring the unit in standby.

Red LED lights up permanently( stand by mode)

The device vibrates three times ( motion detection OFF)

5 Low battery or no memory:

The device vibrates six times .

All LEDs OFF

USB connection:

The device act as a external disk drive when it is connected to a USB port of a computer.

The device vibrates once when it is connected to a powered USB port.

The battery is also charged by the USB port.

During charging the battery, the blue LED is solid and the red LED flashes . The red LED stops flashing when the battery is fully charged

Note:

1.

The timestamp on the pictures and the videos can been set by loading a “ time.txt” document on the external disk drive.

The time file must contain the correct date and time. See example

When the device is powered up again and set into stand-by . The new time will be set and the file time.txt will be erased.

When the battery is disconnected or is completely empty, the time must be set back by loading a time.txt file containing the correct time and date.

2

When the remote control does not work or de red led on the remote control does not lit , replace the battery.

The device can also operate by pushing the buttons on the device body. The buttons are on the side of the board, under the protective film

Product parameters:

| Resolution | 1920*1080/720p |
| --- | --- |
| Power dissipation | 220 mA/h |
| Lens wide angle | 140 degr /oem: 90 degr |
| Lens line long: | 15 cm |
| Memory | Up to 32 Gbyte |
| Frame rate | 30 fps |
| Photo | 4032x3024 |
| Weight | 150 gr |
| Battery | 3800mAh |
| Distance control | 5-8 meter |
| Battery LxWxH | 83x50x10 mm |
| Device body LxWxH | 53x28x10xmm |

Remote controle:

# Text boxes

ON-OFF

USB

mic

LEDS

lever

A

B

C

D

Remote controle

Red LED (lit when pressing a button)

A: switch stand by ( toggle)

B: switch video recording ( toggle)

C: take  photo

A: motion detection ( toggle)

Stand-by=A

Photo=C

Video=B