### WIFI Camera User Manual

### Thank you for using our cameras.Please set your camera correctly in accordance with the instructions in the quick step.

Install APP

·After you enter the URL into the download interface www.scc21.net,according to mobile phone operating system to download and install the appropriate  software to watch.Or scan the QR code on the package to download and install.

·Android Phones can also search“9527”  in “Google play”and download

·iPhone can also search “9527”  in “App Store”and download.

·You can also scan QR code and complete the installation.

LED specification

| 1 | Working condition（Mode） | Red light llllilight | blue light |
| --- | --- | --- | --- |
| 1 | Initialized state (with a card) | Off | On |
| 2 | Initialized state( with a card or being videotaping ) cardccccard） | Off | Blink |
| 3 | Internet status(no card or Pause videotaping） | Long bright | off |
| 4 | Low battery | On | On |
| 5 | Battery charging | No status | No status |

Accession

Connect the power for the first time.

1.First toggle “Start button” boot and wait until the camera  blue light flashing or on(If 60 seconds later the blue light didn’t flashing or on,please long press the reset button for 3 seconds),then use a mobile to  search the WIFI hot spot signals：MD81S （code：12345678）emitted by camera.

2.After the successful connection of MD81S，using a mobile phone to open the operating software →find“local’”page→click“settings” →then select “unlimited network settings” →enter your home router username and password→1 minute later,succeed or failed →If failed , the camera return to the initialized state and the blue light flashing or on→If succeed,the red light flashing or on.（As follow）

（Android）

iPhone

3.After the success of joining the network, select “remote”and then enter the account and password behind the camera body, or scan the QR code ,then you can watch global real-time video(as shown below).

Reasons for the failure to join the network and precautions.

1.Wrong input of the router account password.

2.TF card malfunctioning,please formatting.

3.Router too long without rebooting to assign IP addresses.

4.Close  the router as far as you can for optimal viewing.

TF card recording

Turn off your camcorder,put the TF card into the slot,the camera will automatically record and save.Press the reset  button once，the camera stops recording ideo,and save the current video.Video files saved in 5-minutes a period and the cycle camera.When we need to read TF card file,please use a card reader.

Forget your camera password

1.First toggle “Start button” boot and wait until the camera  blue light flashing or on(If 60 seconds later the blue light didn’t flashing or on,please long press the reset button 3 seconds),then use a mobile to  search the WIFI hot spot signals：MD81S（code：12345678）emitted by camera.

2.After the successful connection of MD81S，using a mobile phone to open the operating software →find“local’”page→click“settings” →then select “unlimited network settings” →enter your home router user name and password→1 minute later,succeed or failed →If failed , the camera return to the initialized state and blue light flashing or on→If succeed,the red light flashing or on.

3.After the success of joining the network,use a mobile to open the operating software ,find “local”page,click “setting”——choose “ system setting”again——“reset to defaults”——wait for 60 seconds （After the successful recovery,there is the original account password.)

Related parameters

| Name | WIFI/P2P network camera |
| --- | --- |
| Video format | AVI |
| initialized state resolution | 640*480 VGA |
| network resolution | 320*240 QVGA |
| Video frame rate | 10fps±5fps |
| Storage | Support TF card storage,expandable up to 32G |
| Support system | Windows ISO Android |
| Charging Voltage | DC-5V |
| Interface Type | Mini 5/8P/Micro USB |
| Storage support | Micro SD Card(TF Card) |
| Type of battery | High-capacity polymer lithium battery |