WSDV-8580Q

User Manual

Content

Introduction	3

Safety Instructions	3

Important Safety Precautions	5

Preparing For Using	6

 Parts Of The Camera	6

 Charging The Battery	7

 Inserting The Memory Card	7

 Installing The Mounts	9

Basic Operation	14

 Turning On And Off The Camera	14

 Setting The Camera	14

 Changing The Mode Of Camera	20

 Recording Video	20

 Taking Still Photos	23

 Playback	24

Making connections	25

 Connecting The Camera To A PC	25

 Wi-Fi Connecting	26

 Connecting The Remote Controller	28

 Connecting The Camera To A HDTV	29

How To Use The PC Camera Function	29

Specification	30

# Introduction

Congratulations on the purchase of your new Action Camera.

This manual contains important safety and operating information. Please read all the information carefully before you use the device to avoid accidents and keep it for future reference. Follow these important safety and operation instructions.

# Safety Instructions

- The Action camera shall not be exposed to dripping or splashing and no objects filled with liquids, such as vases, shall be placed over the product. Dry location use only.

- Keep the camera clean.Never store it next to a heat source or in dirty, humid or wet places.Keep it out of direct sunlight.

- Press the screen and buttons gently. Pressing too hard can damage the product.

- Do not use the camera in an extremely dry environment.

- Do not put the camera in high temperature places (over 40ºC), especially not in a car with the windows closed in summer.

- Do not subject the camera to harsh impacts. Do not drop the unit to avoid damage.

- Do not attempt to dismantle or repair this camera yourself. Qualified personnel should perform repairs.

- Disconnect the camera from the power source before cleaning.

- Use a dry soft cloth to clean this camera.

- This product is not intended for commercial use. Household/personal use only.

- Do not disassemble this unit. To prevent the risk of electric shock, do not remove the cover. No user-serviceable parts inside. Refer servicing to qualified personnel.

- The USB cable for the device should be unplugged from the computer when the unit is left unused for a long period of time.

- Do not subject the product to harsh impacts. Do not drop the appliance. This may result in damage to the product.

# Important Safety Precautions

In order to prevent program failure, never disconnect the product suddenly from a PC while file transferring is in progress.

Disconnect the appliance from PC when cleaning. Use a dry soft cloth to clean this appliance. Do not dismantle the product or use alcohol, thinners or benzene to clean the surface of the product.

Attention: We have done our best to produce a complete and accurate manual. However, we cannot ensure that there are no errors or omissions during the printing process.

# Preparing For Using

## Parts Of The Camera

## Charging The Battery

The camera has an internal lithium battery. Please follow below steps to charge the battery when in first use or in low power.

- Long press the power button to turn off the camera.

2. Open the cover on the side of camera and find the USB slot.

3. Connect the camera to the computer or a charger through the USB cable for battery charging.

4. When charging, the indicator light will turn red and flicker.

5. Once the charging completed,the indicator light will keep red. Please unplug the USB cable.

Notice: The camera body may get warmer after using for long time.This is normal.

## Inserting The Memory Card

This camera is not equipped with an internal memory card. For normal operation,please prepare a TF card(at least class 4) first and follow below steps to insert the card.

- Turn off the camera.

- Open the cover on the side of camera and find the TF card slot. Then insert the card in correct direction.You will hear a “click” sound if the memory card has been inserted into the camera successfully.

| Notice | Must use Class 4(at least) or higher speed rate TF card.Please use above Class 10 TF card when recording video in 4K/1080p@60fps . Please format the TF card before using.Make sure the camcorder is turned off before inserting or removing the card. Using poor quality or counterfeit memory card will lead to many problems such as crashing,can not taking photo or video,damaging the files and so on.Suggest to use brand memory card for improving the stability of camcorder.It has higher requirement for TF card when in moving or long-time continuous shooting. It is important to keep TF card clean.Do not adhere any liquid,dust and particles on the surface of card. |
| --- | --- |

## Installing The Mounts

This camera is waterproof.If the voice cover is tightened,you can use the camera in the water without any waterproof case. In order to using the camera out of doors better,we provide accessary mounts to fix the camera.

There are two kinds of mounts packaged in this camera as below. A is bike mount and B is helmet mount.

Fixing The Camera To A Bike

1. Find the Bike Mount A,fix it to the handlebar of a bike by placing the rubber pad and rotating screws.

2. Choose one connector from the three(a,b,c) shown in below illustration, then fix it to the part 1 of the Mount A.

3. Fix the mounting bracket which has a metal screw(part 2 in below illustration) to the a/b/c connector.

4. Twist the metal screw into the tripod slot of camera.

5. Adjust those screws to make the camcorder more steady and convenient.

Fixing The Camera To A Helmet

1. Find the Helmet Mount B.

2. Choose one connector from the three(a,b,c) shown in below illustration, then fix it to the part 3 of the Mount B.

3. Fix the mounting bracket which has a metal screw(part 2 in below illustration) to the a/b/c connector.

4. Twist the metal screw into the tripod slot of camera.

5. Adjust those screws to make the camcorder more steady and convenient.

6. After finishing installing, use the accessory straps to fix the camera to your helmet.Insert a strap into the two ends of the main mount B, adjust length according to the helmet’s size, and then tie the strap up to your helmet.

# Basic Operation

## Turning On And Off The Camera

- Press the Power/Shutter button to turn on the camera.

- Long press the Power/Shutter button to turn off the camera.

Tips: The working indicator light will turn blue after turning on the camera.

## Setting The Camera

System Setup

1. Turn on the camcorder.

2. Press Mode button to switch to the setting screen as below.

3. Press OK button to enter the function setting screen.

4. Then press Mode button to chose the system setting menu screen as below.

5. Press Down button to scan all menu options.

6. Press OK button to chose and confirm the target menu.

7. Press Mode button to switch to icon ,the screen will show “ Press OK To Exit ”.Then press the OK button to exit.

System setup menu list as below:

| Menu | Function |
| --- | --- |
| Language | Set the language on the screen. Options：【Simplified Chinese】/【Traditional Chinese】/【English】/【Japanese】/【Korean】/【Russian】/【German】/【French】/【Italian】/【Spanish】/【Polish】/【Dutch】/【Portuguese】. |
| Date-Time | Set the date and time. |
| Format | Format your TF card will delete all files including the protected files.Please copy the important files before format. Options：【Confirmation】/【Cancel】. |
| Reset To Factory Settings | Restore the camcorder to factory default settings. Options：【Confirmation】/【Cancel】. |
| Firmware Version | Look up the Firmware information including the model, version, update time and manufacturer. |

Function Setup

1. Turn on the camera.

2. Press Mode button to switch to the setting screen.

3. Press OK button to enter the function setting screen.

4. Then press Mode button to switch to the function setting menu screen as below.

5. Press Down button to scan all menu options.

6. Press OK button to chose and confirm the target menu.

7. Press Mode button to switch to icon ,the screen will show “ Press OK To Exit ”.Then press the OK button to exit.

Function setup menu list as below:

| Menu | Function |
| --- | --- |
| Exposure | Set the exposure value to compensate light.Solve the problems of shooting under poor or strong light. Options:【-3】/【-2】/【-1】/【0】/【1】/【2】/【3】 |
| White Balance | Set the white balance to adapt to different light sources. Options:【Auto】/【Sunny】/【Cloudy】/【Incandescent Light】/【Fluorescent Light】 |
| Image Rotation | The content on display screen will be inverted.You can invert the camcorder to shoot. Press OK button to chose or cancel. |
| Driving Mode | Open/Close the function of driving recorder. Press OK button to chose or cancel. |
| WiFi | Open/Close WiFI. Press OK button to chose or cancel. |
| Light Source Frequency | Set the light source frequency according to your region. Options:【Auto】/【50Hz】/【60Hz】. |
| LED Indicator Light | Open/Close the LED indicator light.Press OK button to chose or cancel. |
| Auto Screensaver | Set the auto screen saver. Options:【Close】/【10s】/【20s】/【30s】. |
| Auto Shutdown | For saving power,the camcorder will close automatically after a pried of time if not using. Options:【Close】/【1minutes】/【3minutes】/【5minutes】. |
| Time Watermark | The date and time will be marked on the video or picture files if open this function.Press OK button to chose or cancel. |

## Changing The Mode Of Camera

The camera has 4 different modes : capture mode, video mode,sport video mode,playback mode. Repeatedly press the Mode button to select one mode.

|  | Video Mode | For recording video. |
| --- | --- | --- |
|  | Capture Mode | For taking still photos. |
|  | Sport Video Mode | For recording slow motion video. |
|  | Playback Mode | For playing the recorded files. |

## Recording Video

1. Turn on the camera,press the Mode button to switch to video mode.

2. Start to record video.

- Use the LCD screen to view your subject.

- Press the Shutter button to start recording.

- The record duration will be shown on the LCD display.

- If using a low speed card, the video size will be adjusted to 720P automatically.

3. Finish recording.

- Press the Shutter button again to stop recording.

- The camcorder will stop recording automatically once capacity of the memory card is full.

Notice:

1. When recording video,if you want to record voice at the same time,please unscrew the voice cover with a coin.Then you can record voice.

2. When using the camera in the water,please tighten the cover for avoiding water damage the camera.

Video mode menu list as below:

| Menu | Function |
| --- | --- |
| Video Resolution | Set the video resolution. Options:【720P 30FPS】/【720P 60FPS】/【720P 90FPS】/【1080P 30FPS】/【1080P 60FPS】/【 2.7K 30FPS】/【 3.2K 30FPS】/【 4K 15FPS】. |
| Recording Sound | Open/Close the sound during recording video.Press OK button to chose or cancel. |
| Time-lapse | Set the time-lapse recording. Options:【Close】/【0.5s】/【1s】 /【2s】/【5s】/【10s】 /【30s】/【60s】. |
| Loop Recording | Set the time of loop recording. Options:【Close】/【2minutes】/【3minutes】 /【5minutes】. |
| Slow Motion | Set the slow motion resolution. Options:【1080P 60FPS】/【720P 90FPS】. |

## Taking Still Photos

1.Turn on the camera,press the Mode button to switch to capture mode.

2.Start to take a still photo.

- Use the LCD screen to view your subject.

- Press the Shutter button to take a photo.

Capture mode menu list as below:

| Menu | Function |
| --- | --- |
| Photo Resolution | Set the size or resolution of still photos. Options:【2M】/【5M】/【8M】/【12M】/【16M】. |
| Timed | Set timed photographing.Press shutter button,camera will take a photo after automatic countdown. Options:【Close】/【3s】/【5s】/【10s】/【20s】. |
| Auto | Set automatic photographing.Press shutter button,camera will take photos continuously after automatic countdown. Options:【Close】/【3s】/【10s】/【15s】/【20s】/【30s】. |
| Drama Shot | Set this function to take several photos in one second. Options:【Close】/【3P/s】/【5P/s】/【10P/s】. |

## Playback

1. Turn on the camera,press the Mode button to switch to playback mode.

2. Press Down button to view photos and video files .

3. Playback the video

- Press the Shutter button to start playing the video files.

- Press the Shutter button again to have a pause.

- At last, you can press Mode button to exit current video playing.

4. Delete Files

In playback mode, keep pressing the Mode button for two seconds. A message box about delete information appears on the screen. You can press Down button and OK button to chose confirmation and delete the current file.

# Making connections

## Connecting The Camera To A PC

There are two ways to download files from the memory card to a computer:

1. Insert the memory card into a card reader.

2. Connect the camera to a computer through the supplied USB cable.

Using a Card Reader

1. Take out the memory card from the camera，then insert it into a card reader which is connected to a computer.

2. Open [My Computer] or [Windows Explorer] and double-click the removable disk icon that represents the memory card.

3. Copy the files to the chosen directory in the computer.

Connecting Camera to a PC by the USB Cable

- Connect camera to a computer through the supplied USB cable, then turn the camera on. The screen will display”USB Mode”,”PC Camera”,”Charging Mode”.Press Down button to choose”USB Mode”,then press OK button to enter USB mode.

2. Open [My Computer] or [Windows Explorer]. A"Removable Disk" appears in the drive list. Double-click the "Removable Disk" icon to view its contents. Still photos are stored in the folder named "Photo". Movie Clips are stored in the folder named "Video".

3. Copy the files to the chosen directory in the computer.

## Wi-Fi Connecting

Download and install APP in Pad or smartphone, you can operate camcorder remotely.The functions include shooting,setting the camcorder and preview photos or videos, it will be more convenient to control.

Step 1: Download the APP "SportCam”.

Search and download APP named "SportCam" from “Apple App Store “or “Google Play “.Then install it on your Pad or smartphone.

Step 2: Open camcorder’s Wi-Fi.

Press Wi-Fi button,the screen will appear icon.Waiting for at least 5 seconds,Wi-Fi account and password will show on the screen.

Step 3: Connect camcorder’s Wi-Fi

Open Wi-Fi search on smartphone or Pad.Search camcorder’s Wi-Fi account.Input the initial password "66666666".Then click to link.

Step 4: After connection is successful, open APP "SportCam" on the smartphone or Pad.You can take photos,record videos, playback files and set the camera on phone.

Step 5: Press Wi-Fi button will exit Wi-Fi.

## Connecting The Remote Controller

1.LED indicator light

2.Shutter button

3.Stop button

4.Power button

5.Battery slot cover

6.Battery slot lock

Preparing :Push the battery slot lock, and open the battery department cover , then insert a battery (1.5 V, AAA) into the battery slot. Please pay attention to the pole (+) mark on the battery for proper function.Before using the remote control, please confirm the camera have turn on.

• Press the shutter button to start recording, the LED indicator light keep blue and flash.

• Press the stop button to stop recording video.

• Press the power button to stop recording,the screen of camera will close at the same time.Then the camera is turned off.

## Connecting The Camera To A HDTV

Connect the camera to a HDTV through the HDMI cable.Turn on the TV and set it to HDMI mode,then turn on the camcorder. After successful connection, the camcorder’s screen will display on the HDTV.The screen will turn black.Then, press Mode button to enter playback mode and press OK button to view the video or pictures on the HDTV.

# How To Use The PC Camera Function

1. Connect camera to a computer through USB cable.

2. Turn on the camera.Press Down button to choose “PC Camera Mode”.The screen will appear camera lens.

3. In Window XP system,open [My Computer],double click “USB video tool”.The camera will work as PC camera.In Window Vista, 7 and 8 system, the PC camera function can only be used for communication software (Skype,QQ etc.)

4. Press Power button to exit PC camera mode.

# Specification

| Image Sensor | Sony 8 Mega Pixels CMOS |
| --- | --- |
| LCD display | 2.0", 960*240 TFT |
| Resolution | Image:2M /5M /8M /12M /16M Video:720P 30FPS/720P 60FPS/720P 90FPS/ 1080P 30FPS/1080P 60FPS/2.7K 30FPS/3.2K 30FPS/4K 15FPS |
| Aperture | F2.2, f=2.65mm |
| Lens feature | 6G Wide Lens ,FOV 150 |
| Focus | 1.5m~infinity |
| White balance | Auto,Sunny,Cloudy, Incandescent Light, Fluorescent Light |
| Exposure | +3.0 EV ~ -3.0 EV in 1.0EV increment |
| PC Camera | Yes |
| Video out | HDMI |
| PC interface | Micro USB 2.0 |
| Microphone | Built-in |
| Speaker | Built-in |
| Storage | Micro SD card, up to 64GB |
| Power source | Built-in Li-ion rechargeable battery 1000mAh |
| Supported O/S | Microsoft Windows XP, Vista, win7/Mac 10.5 or above |
| Dimension | 68*49.5*37.8mm |

# Text boxes

- Power/Shutter/OK Button

- Mode Button

3. Lens

4.Working/Charging Indicator Light

5. Wi-Fi/Down Button

6. Voice Cover

7. LCD Screen

8. HDMI Jack

9. Reset

10. USB Jack

11. TF Card Slot

12. Tripod Slot

Mount A

Mount B