S01 1080p Camera module instructions

1. Basic operations：

1） Boot: click the power button close to power line. Long press button A, until both blue & red lights flash, loose the button, then the red bright keeps on. It’s in the standby mode.

2） Video Recording:

Short press button B, the red will light flash twice and then light off. Short press button B again,red light is on, save the video.successfully.

Press button A, both red & blue flash 3 times, turn off the device.

The video saved automatically every 5 minutes. Auto-cycle recording after memory card fully.

3） Photograph：In standby mode, red light keeps on. Short press button C, both blue & red lights flash once, and device shakes once, it means shoot successfully.

4） Motion Detection: In standby mode,red light keeps on. Short press button D, both blue & red lights flash twice, then both lights go off. It’s in the motion detection mode. Short press button D again, the device shakes twice and red light keep on. Save video successfully. Press button A to turn off the device.

2. Video while charging:

1）Turn on the power button before charging by USB. When charging, the red light keeps on and blue light is flashing. After charging full, the blue light will stop flashing.

2）Video: When charging by USB line, press button B, the device shake once and red light flashes 3 times then goes off. It is in video mode. Press button B again, the device shakes and red light keeps on, save video successfully. Press button A to turn off the device.

3）Photograph and motion detection: in addition to the red light shows USB electricity long flashing, other operations are the same as basic operations.

3. Product Parameters:

| Items | Relative Parameters |
| --- | --- |
| Video format | M-JPEG |
| Video code | AVI |
| Video resolution | 1920*1080 HD |
| Video frame rate | 30fps |
| Battery capacity | 420 mA (extra battery capacity :3800mah) |
| Working time | 70-80 mins ( about 10 hours with 3800mah extra battery ) |
| Power consumption | 220mah |
| Device ( L*W*H) | 53*28*10mm |
| Charging voltage | DC-5V |
| Interface type | Mini 5Pin USB |
| Storage support | TF card up to 32GB |
| View angle of lens | 90 degree, 140 degree |

4. Changing time：built a document “timerset” in the memory. Content: 2015.05.12 09:07:00 y, you can change the number to change the time, then save it.

Note: need to reset the time again after power loss.

Eg.：2015.05.12 09:07:00 y

means: 7past 9 o’clock on May 12th 2015, and sign time on the screen.

y means: sign time on the screen;

n means: not sign time on the screen.

5. Note:

1.Formatting TF card: Turn on the power button, press the button A to start up, then press button D about 3 seconds, the motor in the device will vibration, means finish TF card formatting.(after long time using, the TF card will slow down, need to be formatted to make it faster. Please avoid to format TF card via computer. )

2. This camera built-in 420mA Li-battery, need 4-5 hours to charging.

3. It can be charged by mobile power supply.

4. When the voice in the video not clear or has noise, please charge the device in time.

5. When not in using, please turn off the camera to save electricity.